## Slide 1
SIDE-CHANNEL
CRYPTANALYSIS
AES KEY RECOVERY
via Machine Learning on Power / EM Traces
Replication of Poudel & Rahimi (arXiv:2508.11817, 2025) on the ASCAD dataset,
with three extension milestones: architecture comparison, multi-task learning,
and desynchronization robustness.
Aaryan // Laboratory Project // 2026

## Slide 2
ROADMAP
What we'll cover
01
The Threat
What a side-channel attack is, and what the attacker sees vs. recovers
02
The Dataset
ASCAD electromagnetic traces, labels, and the attack pipeline
03
The Metric
Why raw accuracy is meaningless here — Key Rank / Guessing Entropy
04
The Models
Random Forest, SVM, CNN, ResNet, multi-task ResNet
05
Three Milestones
Baseline -> architecture study -> five extension experiments
06
The Result
Key byte #2 recovered: 0xE0, correctly, in ~1,360 traces
02

## Slide 3
THE THREAT
AES is unbreakable... on paper
AES-128 has no known practical mathematical attack. But a physical chip leaks information while it computes: power draw and electromagnetic emissions vary with the data being processed. That leakage is a side channel — and it can be learned by a model.
The target
An AVR microcontroller (ATMega8515) running textbook AES-128 encryption.
The leakage
Electromagnetic emissions captured as a 700-sample trace per encryption.
The goal
Recover the secret key from traces + known plaintexts — never the key itself.
EM TRACE (SAMPLE)
highlighted window: leakage of the masked S-box operation for key byte #2
~10,000 attack traces x 700 samples each
public dataset: ANSSI / ASCAD (CHES 2018)
03

## Slide 4
THREAT MODEL
What the attacker has vs. what comes out
GIVEN TO THE ATTACKER
~10,000 EM power traces (700 samples each)
the plaintext of every encryption (public)
the ASCAD device's leakage model / trace format
NOT given: the secret key
RECOVERED BY THE MODEL
ONE KEY BYTE
0xE0
key byte #2 of 16 — the ASCAD benchmark target
correct — matches the true device key exactly, using ~1,360 attack traces
04

## Slide 5
METHODOLOGY
The attack pipeline, end to end
1
Raw traces
50k profiling + 10k attack traces, 700 samples
->
2
Preprocess
Standardize (fit on profiling only)
->
3
Model
P(class = Sbox(p XOR k) | trace)
->
4
Key-rank
Accumulate log-likelihood over 256 key guesses
->
5
Recover
True byte reaches rank 0
score(g) = sum_i log P( class = Sbox(plaintext_i XOR g) | trace_i )
Rank the true key byte among all 256 hypotheses g. Rank 0 = recovered. This is what actually measures attack success — not classification accuracy.
05

## Slide 6
EVALUATION
Why "accuracy" is the wrong scoreboard
Top-1 accuracy on the 256-class problem is 0.4-1% — barely above the 1/256 = 0.39% random-guess floor. A model that looks almost useless can still fully recover the key, because a tiny per-trace bias compounds over thousands of traces.
ACCURACY (misleading)
0.67%
CNN top-1 accuracy — chance is 0.39%. Looks almost random.
If you selected models on this metric, you'd throw away the one that actually works.
KEY RANK (ground truth)
RANK 0
by ~1,360 attack traces — the true byte is ranked #1 out of 256 hypotheses.
This is the metric used for every model comparison in this project.
06

## Slide 7
MODELS UNDER TEST
Five model families, one benchmark
Random Forest
300 trees, tabular baseline
Weak
SVM (PCA-50 + RBF)
subsampled to 10k, O(n^2) cost
Weak
CNN (Zaid, compact)
~17k-param 1D conv net, one-cycle LR
Recovers
ResNet (1D, residual)
deeper, kernel-11 + SELU blocks
Recovers + robust
Multi-task ResNet
shared trunk, 3 joint heads
Best (fixed-key)
07

## Slide 8
MILESTONE 1 - BASELINE
Random Forest vs. CNN — the first result
RANDOM FOREST
0.46%
attack accuracy (chance 0.39%)
never converges
CNN (ZAID, 1D)
0.67%
attack accuracy
rank 0 by ~1,360 traces
08

## Slide 9
MILESTONE 2 - ARCHITECTURE
ResNet vs. CNN on the harder variable-key set
TRACES TO RANK 0
CNN, variable-key
516
ResNet, variable-key
276
ResNet, fixed-key
868
CNN, fixed-key
1,362
On the harder variable-key dataset, the ResNet needs under half the traces the CNN does — the paper's qualitative finding, reproduced.
09

## Slide 10
MILESTONE 3 - EXTENSIONS
Six threads, stress-testing the pipeline
a
SVM baseline
Rank 138, no recovery — confirms only CNN/ResNet exploit the leakage
b
Multi-byte attempt
Bytes 3-4 stuck at chance — data-limited, not a modeling failure
c
Multi-task ResNet
3x fewer traces on fixed-key (270 vs 868) via auxiliary mask heads
d
Desync robustness
CNN collapses under jitter; ResNet still recovers the key
e
Seed variance
276 vs 1,540 traces across 2 seeds — single-run results can mislead
f
Shuffled-label control
Accuracy = exact chance (0.388%) — no label-artifact shortcut
10

## Slide 11
MILESTONE 3C - MULTI-TASK LEARNING
Auxiliary heads break the training plateau
3x
fewer traces to recover the key, fixed-key set (270 vs. 868 for single-task ResNet)
But not a free lunch
On the harder variable-key set, the auxiliary heads add noise instead of signal: 3,374 traces vs. 276 for the plain ResNet — worse, not better.
11

## Slide 12
MILESTONE 3D - ROBUSTNESS
Misalignment breaks the CNN, not the ResNet
TRACES TO RANK 0
aligned
desync50
desync100
CNN
1,362
no recovery
no recovery
ResNet
868
608
979
The compact CNN has zero shift tolerance — any tested jitter drops it to chance. The ResNet still recovers the key at both jitter levels, with only a modest trace penalty.
12

## Slide 13
THE RESULT
The recovered byte, end to end
true key: 4d fb e0 f2 72 21 fe 10 a7 8d 4a dc 8e 49 04 69 byte #2 recovered correctly, ~1,360 traces
13

## Slide 14
METHOD NOTES
Where this replication departs from the paper
Target byte
byte 2 (community standard — ASCAD masks only bytes 2-15)
CNN architecture
compact ~17k-param net (Zaid et al.), not the 60M-param VGG head — the VGG memorizes and never ranks the key here
Model selection
checkpoint chosen by validation Guessing Entropy, not validation loss — CE loss is flat/rising for ~20 epochs while the attack is already improving
Full-key recovery
out of scope — the extracted .h5 is a trace window around byte 2 only; bytes 3-15 need the ~60GB raw capture
14

## Slide 15
TAKEAWAYS
What this project shows
A tiny per-trace statistical bias, invisible to top-1 accuracy, is enough for a neural net to fully recover a real AES key byte.
Architecture matters more than the paper's framing suggests: the ResNet beats the compact CNN specifically where alignment is imperfect.
Multi-task auxiliary losses can break the masked-SCA training plateau 3x faster — but only help on the dataset they were tuned for.
A shuffled-label control confirms the whole pipeline is exploiting real leakage, not a label-distribution artifact.
15

## Slide 16
Thank you
Questions? — code, report, and results at the project repository
python -m src.demo · README.md · report/ASCAD_replication_report.pdf